Mass balance of Mårmaglaciären 2004/2005

Rickard Pettersson

Department of Earth Sciences, Uppsala University

Villavägen 16, SE-752 36 Uppsala, Sweden

Summary

The winter accumulation on Mårmaglaciären was surveyed by Peter Jansson, Henrik Törnberg, Erik Sarri, Per Holmlund and John Hult on April 13, 2005. The snow density was measured with a PICO-drill in the northern, and the mean snow density was calculated to 0.47 g cm-3. From the density profile, cumulative water equivalents was calculated and a linear relationship between cumulative water equivalents and depth was established (Figure 2).  The winter balance map was determined from 151 snow probings on the glacier (figure 3). The conversion of snow depths into water equivalent values were done by using the empirical relationship between cumulative water equivalents and depth (Figure 2).  The total winter balance for the glacier was determined to 1.11 m w. e (Figure 4, Table 1).  Four new ablation stakes was also established during spring (Figure 5) and the summer balance was determined by stakes measurements on September XX by Henrik Törnberg. The ablation gradient was determined to be -0.49 m w.e. / 100 m from linear regression (Figure 6).  The total summer balance amounted to 1.90 m w.e. (Figure 7, Table 1). The summer and winter balance yield a net balance of -0.79 m w.e., ( Figure 8, Table 1) and concludes the 16 mass balance determination on Mårmaglaciären. The equilibrium line altitude (ELA) was to 1640 m a.s.l (Figure 10). The ration between accumulation area and total area (AAR) was estimated to 14% (Figure 11).

Figure 1: Snow Density at the northern cirque of Mårmaglaciären.

Figure 2: Cumulative water equivalents plotted against depth. The linear fit between the two was used to convert snow probings to water equivalents.

Figure 3: Map of snow dept soundings.

Figure 4: Winter mass balance map for Mårmaglaciären.

Figure 5: Map of stake locations for Mårmaglaciären.

Figure 6: Ablation as function of elevation based on ablation stake measurements.

Figure 7: Map of the summer mass balance of Mårmaglaciären

Figure 8: Map of the net mass balance of Mårmaglaciären

Figure 9: The mass balance record for Mårmaglaciären.

Figure 10: Winter, summer and net balance as a function of elevation for Mårmaglaciären.

Figure11: The net volume change and area distribution on Mårmaglaciären.